## Slide 1
Applications of GIS
  Week 11
  Some more demonstrations
  Q&A for A4

## Slide 2: What are we going this week
Looking at elements at risk, vulnerability
How to present risk for each of these
Making some maps, how will they fit into your report?
Q&A

## Slide 3: Vulnerability maps
You can create your vulnerability maps using two different methods. Those are:
Create separate vulnerability maps and combine them into one vulnerability map (possibly weighted), like you did with your hazard maps. Your risk map would therefore be your hazard x vulnerability map.
  Risk equation = Hazard x Vulnerability x (4 elements at risk maps)
Create your vulnerability maps based on the four requirements used in your analysis (population, environment, industry and infrastructure). You would need to create four maps and your vulnerability would be related to each of these categories. Then, create a combined vulnerability and elements at risk map for each of the four requirements.
  Risk equation = Hazard x (4 Vulnerability x elements at risk maps)

## Slide 4: Vulnerability maps examples
There is a large list of data that you can use for your vulnerability maps and you are advised to do some research, but here are some examples:
Population density
  Census data from Assignment 2 will be used to calculate this.
  Follow the steps from the census assignment and calculate a population density field
  Population density = Total People/ Area
Age distribution
  Younger or elderly people may be more likely to be affected e.g. cannot drive.
  Use census data again and calculate a vulnerability age group based on age distribution to map out
Distance to hospitals, distance to emergency facilities
  Euclidean distance tool as demonstrated last week

## Slide 5: Elements at Risk and Vulnerability: Some Bushfire Examples
Constraint | Process | Potential Vulnerability Value
Hospital Points | Extract Values to Points | Number of Patients
Agriculture Polygons | Zonal Statistics Tool / Extract by Mask | Production Type
Fire Infrastructure | Extract Values to Points | Building Material
Environmental Conservation | Zonal Statistics Tool / / Extract by Mask | Flora / Fauna Endangered Rating
Population (By SA2 Region) | Zonal Statistics Tool | Age, Population Density, Disability

## Slide 6: Elements at risk maps
Elements at risk can be categorized to your four requirements:
  Industry
  Population
  Environment
  Infrastructure
You need to have examples of all four.
It is recommended to create maps for each separate element at risk to be able to know the risk of each one. You can create a combined map at the end if you want.
E.g. Infrastructure – risk map for roads, train stations etc.

## Slide 7: Creating elements at risk layers/ maps
Points
  Extract Values to Points tool
    Extract the hazard values to your points
  Right click data and change symbology to the same as your Hazard/ risk layers
  Change symbol if needed
  Select properties to change the size of the symbol
Lines
  Use the buffer tool to create a buffer around the line
  Clip Raster for hazard map to the buffer raster
  Change symbology to the same as hazard maps
Polygons
  Zonal Statistics Tool = Calculates, Average, Maximum, Minimum raster value for polygon areas, per attribute (e.g. Per SA2 region)
  Extract by mask tool = Clips the raster to the polygon area

## Slide 8: Presentation of your maps

## Slide 9: ArcGIS online
Upload TIFs and Shapefiles (must zip all files together beforehand)
Maybe show hazard map and different elements at risk on different layers?
Choose map output style and share URL