## Slide 1
Applications of GIS : Week 6
  Assignment 2 Feedback
  Assignment 3 Run through

## Slide 2: Feedback from assignment 2
Overall everyone did a very good job, especially considering the circumstances
The mapping conducted was good for first maps produced, although for some maps the layout could be improved, have a strong focus on the maps (larger) and then also position the legend and title a little more clearly, don’t leave too much white space want to show as much information as possible. Also good have a location map to show where your project areas are in context of Melbourne or Victoria.
Methodology, most people wrote good clear and concise explanations of what tools were used, what data was used and how their trends were calculated. Although there were some reports with very detailed methods like the workflow (this is not required, keep it concise) and some people wrote about their results in the methodology (this should be in results or discussion section).
The discussions were good there was a good summary of the findings and recommendations given, although would have been good to see more information from external sources to backup your statements. Some people also did not discuss the limitations of their analysis and further analysis to be conducted, this is very important for the next two assignments.

## Slide 3
Demonstration
A quick run-through of assignment 3

## Slide 4: Analysis for high speed rail
Data:
Proposed rail alignments
Digital Elevation Model
Requirements:
Cannot be over a slope of 25 degrees
Cannot follow a path prone to flooding
Total Distance of each alignment
Total number of metres each alignment climbs or falls
Number of unsuitable terrain obstacles each alignment encounters
Other requirements
Near townships
Water crossings
Infrastructure crossings

## Slide 5: Requirement: Cannot be on a slope of over 25 degrees
Generate points along line tool at 20 m intervals (the size of the raster pixels) for the VRA layer.
Extract values to points tool using the slope layer.
Right click the generated layer and check the attribute table.
The RASTER VALUE column will show the slope value for each pixel of each alignment.
Can export this data and calculate the amount of points with a slope over 25 degrees per alignment or right click the raster value column and select statistics.
Can also use Greater than or Equal function to do this – simpler

## Slide 6: Requirement: Cannot follow a path prone to flooding
Multiple methods:
  Method 1:
    Download Data.vic.gov flood data
    Find the intersection of the flooded extent area of each alignment
  Method 2:
    Calculating a flow accumulation
    Use the Fill tool with the DTM
    Then use the Flow Direction tool (not raster function)
    Then use the Flow Accumulation tool
  Method 3:
    Visual interpretation from base maps
    We do NOT recommend this

## Slide 7: Requirement: Total number of metres each alignment climbs or falls
Export each alignment to its own layer
Generate points along line at 20 m each
Get change in elevation:
  Math raster function
  20*Tan(slope*(pi/180)) – see image for description
Extract change in elevation raster values to points
Select points attribute table
Right click raster value
Select summary statistics and get the total sum

## Slide 8: Length and 3D length of each alignment
Attribute table of alignments
Add a new field/ column
Right click the new column and select calculate geometry
Select length and run
For 3D length need to first interpolate shape with DTM
  Use the Interpolate shape tool to interpolate the DTM z values to the proposed alignment
  Right slick the new layer’s attribute table to get the 3D length

## Slide 9: Steps to help complete the assignment
Steps:
Get data, make new GDB, make it default GDB
Show just 4 options, definition query
Load in DEM, change symbology to Classify, 10 classes, elevation colours
Clip raster
Slope raster function
Get slope >= 25 degrees, Greater than Equal raster function, select raster, raster 2 = 25
Get change in elevation
  Math raster function
  20*Tan(x*(pi/180))
Flow Direction tool (not raster function)
Flow Accumulation tool
Limit to > 50,000 (shows rivers)
Generate Points Along Lines (20 Meters)
Extract Multiple values to points
Summarize Attributes
Add surface information Tool (multiple attributes including surface length)
Get 100 year flood extents, clip lines to extents, calculate length

## Slide 10: Other assignment notes
Remember to change to the correct coordinate system at the beginning of the assignment
Literature Review
  Must be supporting your analysis
  Sample literature available on the LMS
Self reflections
  Add at the end of the assignment
  Each group member must do this
Data sources:
Good list: https://myvictoria.vic.gov.au/data-sources
Data search: https://www.data.vic.gov.au/

## Slide 11
Questions and Queries?